## Slide 1: Interpolation methods for 3D geological modelling
Lachlan Grose, Laurent Ailleres, Gautier Laurent, Fernanda Alvarado.

## Slide 2: What is a geological model
Numerical representation of the geometry and distribution of geological objects
Topology of geological objects
Geological units
  Boundary representation (surfaces)
  Volumetric representation
Discontinuities
  Representation of geometry (surface)
  Effect on other features
    Faults
    Unconformities
Wellmann and Caumon 2018

## Slide 3: How to build surfaces?
2D equivalent is contouring value data
- manually contour
- interpolate value onto grida
- contour using marching squares

## Slide 4: Methods for representing geology
Explicit | Implicit
Surface geometry collocated with the representation of the surface | Surface is extracted from an isovalue of an implicit function
Topology is defined by the geometry of the surfaces | Implicit function approximated from observations
Update of surface geometry is difficult | Each feature is represented by a different function, multiple surfaces  same function
Surface geometry is controlled by geologists knowledge | Quick to update and reproducible
Subjective and time consuming | Knowledge is difficult to incorporate
One support per surface | Topology defined by order of Boolean operations
Explicit representation
Implicit representation
Wellmann and Caumon 2018
19 surfaces
6 Implicit functions

## Slide 5: Implicit modelling constraints
Gradient normal constraints
Gradient tangent constraints
Scalar value constraint
Interface value constraint
f(X) – f’(X) = 0
f(X) – f’(X) = 0

## Slide 6: How implicit modelling works
Least squares minimisation
Balance regularisation and observation constraints
Solve linear system of equations
Exact fit of function and observations

## Slide 7: Implicit surface modelling
Calgagno et al., 2008; Chiles et al., 2004; Cowan et al., 2003; Frank et, al., 2007; Hillier et al., 2014; La-junie et al., 1997; Mallet 1992,14
Approximate implicit function from geological observations (contacts, strike and dip) using weighted combination of basis functions
  Data supported
  Discrete approach
Implicit function can be evaluated anywhere in the model volume defining stratigraphic thicknesses
Surfaces are extracted by tracing isovalues (3D contours) of the implicit function

## Slide 8: A case study
Surface locations sampled from flat plane
Surface locations sampled from a flat plane with noise added

## Slide 9: Comparing interpolators
Discrete:
Piecewise Linear interpolator
Discrete:
Finite difference interpolator
Data supported:
Surfe Radial Basis Interpolation
Single isosurface has topology suggesting multiple surfaces

## Slide 10: Adding smoothing to RBF
Increasing smoothing
Shift location of smooth surface
Topology of surface is better

## Slide 11: Varying regularisation
Increasing smoothing
Low regularisation fits data points better

## Slide 12: Comparing interpolators
Radial Basis function Interpolator: Interface constraints
Finite Difference Interpolator: Interface constraints
Piecewise Linear Interpolator: Value constraints

## Slide 13: Understanding the differences
Outcrop | RBF interface | PLI value | FDI interface
 | Circular blob, resulting from flipped polarity vectors | Smooth fold limb | Small artefact but smoothed
 | Fold hinge with outcropping purple blob | Fold hinge | Fold hinge with outcropping purple blob
 | Circular feature outcropping orange and purple | Antiform hinge with green surfaces | Circular feature with green surfaces
 | Basin | Saddle | Saddle with part of basin
 | Slightly folded limb | Smooth fold limb | Slightly folded limb

## Slide 14: Adding unconformities

## Slide 15
Three coordinates – three scalar fields
Major structural feature
  fault surface
  fold axial surface
  intrusion major axis
Structural direction
  fault slip direction
  fold axis
  intrusion flow direction
Additional direction (if required)
  Fault , e.g. fault extent
The Structural Frame concept

## Slide 16: Faults using step functions
Calcagno et al 2008

## Slide 17: Problem with step functions
Fold hinges are not faulted… only scalar field value changed!
True fault kinematics
Step function
Pure dextral strike slip fault in map view

## Slide 18: Shrinking intrusions?
Map view of an implicit function of a pure strike slip faulted scalar field using step functions

## Slide 19: Apply fault to an existing surface
Godefroy et al 2018

## Slide 20: Problems
Fault splays?
Folded stratigraphy?
Intrusions?

## Slide 21: Direct kinematic integration

## Slide 22: Fold structural frame
Hinge
Limb
Point of inflection?
½ Wavelength
Point of inflection?

## Slide 23: Implicit Fold Modeling: fold frame
Fold Frame F = (X,Y,Z)
  Based on the finite strain ellipsoid
Relative orientation of deformed foliation.
  Local rotation within the fold frame.
    Fold axis rotation angle (αp)
    Fold limb rotation angle (αL)
Si-1
X
Z
Y
αp
αp
αL
αL
Laurent et al., 2016, EPSL

## Slide 24: Time-aware Geometrical modelling – combining structural frames
Poly-deformation:
  Modelling events step by step
  Time-aware process: youngest event is modelled first, then the second youngest, etc… until the primary foliation (most often bedding) is modelled
Modelling is geometry based (not mechanical)
Event types:
  each fault or family of faults
  Folding event
  Unconformity
  Intrusions
S2
S1
S0
F2
F1
S1+
S2+
S1+
S0+
S0+
Laurent et al., 2016, EPSL

## Slide 25: Intrusion Structural Frame
Step geometry, sill (Hutton, 2009)
Magma flow
Fernanda Alvarado-Neves (PhD candidate, Monash University

## Slide 26: Intrusion Structural Frame
Step geometry, sill (Hutton, 2009)
Magma flow
Fernanda Alvarado-Neves (PhD candidate, Monash University

## Slide 27: Intrusion Structural Frame
Fernanda Alvarado-Neves (PhD candidate, Monash University
N

## Slide 28: Summary
Implicit modelling is approximating a signed distance function representing the “stratigraphic” distance
Can include:
  Contact locations, or location within a stratigraphic series
  Orientation data
  Form surfaces
  Fault geometry/kinematics
  Fold overprinting relationships/foliations
  Intrusion anisotropy
Assumes:
  Constant(ish) stratigraphic thickness
Can’t use:
  Lithology
  Inequalities

## Slide 29: LoopStructural
Core 3D modelling algorithms behind Loop
Python library for 3D geological modelling
  Discrete interpolation using finite difference method and piecewise linear method
  Fold interpolator (Laurent et al., 2016)
  Implicit fault kinematics (Grose et al., in prep)
Open source (MIT license)
Available on PyPI and Github (pip install LoopStructrual)
Linked with map2loop for automatic model generation
Export surface meshes as vtk, obj
Preprint in Geoscientific Model Development
www.github.com/Loop3d/LoopStructural

## Slide 30: Recent research
Use structural frames for characterising geometry of different geological objects
  Lithologies?
  Resource models?
Build lithology models
  Relax/remove thickness constraints
  Use only inequality constraints
  Adapt mathematical techniques from geophysics/machine learning to improve data types used for implicit modelling

## Slide 31: Modelling using inequalities
>
>
Constraints
Orange > brown and yellow
Brown < orange and > yellow
Yellow < orange and brown
Function should be as smooth
as possible

## Slide 32: Adding inequality constraints
where A is the regularisation matrix from discrete implicit modelling
  Minimise second derivative of the objective function
Inequality constraints
  For each iteration
  Upper constraints are applied by updating v using the max(v,l)
  Objective function to minimise is
  Use stochastic gradient descent method for optimising objective function, here we will use ADAM optimiser.

## Slide 33: An example

## Slide 34: Another example

## Slide 35: Summary
Using existing interpolation framework from LoopStructural inequalities are incorporated using fast optimisation algorithms
ADAM optimiser in optax the model can be solved in 6 seconds compared with 5 seconds for linear least squares using scipy. Negligible time increase!
Challenge to balance both regularisation and inequality constraints -> model is not satisfactory near boundary between data values
Modelling using inequality constraints focused on high data density environments e.g. mine scale models where thickness is more variable and may not be known.
Optimisation frameworks can allow for different types of constraints to be included at minimal cost.
Hillier et al 2022 have used a similar approach but have represented the implicit function using a neural network