## Slide 1
Loop ‘Flow’
Guillaume Pirot, Leonardo Portes, Mark Jessell,
Kerry Bardot & Jim McCallum
guillaume.pirot@uwa.edu.au
Fremantle, July 23rd 2023
6ias 3D modelling and Loop workshop
Notes: The University of Western Australia acknowledges that it is situated on Noongar land, that the Noongar people remain the spiritual and cultural custodians of their land and continue to practise their values, languages, beliefs and knowledge.
Welcome……
Excuse our Director Steve who is unfortunately ill and cannot be here….
Program for today…..
Step a back a bit and tell you what we are all about……

## Slide 2
Majors, METS and Survey Participants (16)

## Slide 3
Research Participants and Affiliates (20)

## Slide 4: What is LoopFlow ?
A Python package authored by Mark Jessell and Guillaume Pirot, to:
  Generate graphs from Loop models
  Calculate flow parameters based on those graphs
Available on GitHub:
  https://github.com/Loop3D/LoopFlow
With some example Python notebooks:
  one derived from ‘Draw your own model’ example (6ias map2loop workshop)
  the other hardwired to loading van der Wielen et al. Emmie Bluff Gocad surfaces

## Slide 5: Motivations – part 1
Understanding and Targeting Mineral Systems
  Source
  Path
  Host
Testing different scenarios
  Source locations
  Potential path or barriers
  Potential hosts

## Slide 6: Motivations – part 2
Groundwater management
Subsurface characterization
Inverse problem
  Challenging computing costs of flow and transport simulations with finite element or finite difference solvers

## Slide 7: From voxet to graph
Voxet outputs from Loop Model

## Slide 8: Graphs

## Slide 9: Possibilities
Does it work to approximate flow and transport
in aquifers with complex structures?

## Slide 10: Mineral resources perspectives
Distance from source
Preferred pathways
Path scenery
Mineralization halo
Contaminant remobilization
Chemical reaction paths
Python notebook: https://github.com/Loop3D/6IAS/blob/main/LoopFlow/2_m2l_wa_flow.ipynb

## Slide 11: A groundwater application
Can we approximate flow and transport simulations by computations through graph representations of subsurface models?
Darcy’s law
Advection dispersion equation (ADE)
advection
diffusion

## Slide 12: Experimental setting
7km x 5km x 1km (x-axis,y-axis,z-axis)
70 x 50 x 40 cells
3 heterogeneous stratigraphic units
3 faults (fixed geometry)
Log K (m/d)
Z (km)
Y (km)
X (km)
X (km)
0
7
0
7
0
5
1
0

## Slide 13: Scenarios & boundary conditions
Scenario 0
Scenario 1
Scenario 2
Scenario 3
Scenario 4
Scenario 5
Scenario 6
Scenario 7
Fault 1
Fault 2
Fault 3
General flow direction
No flow
No flow
Head = 100m
Head = 0m
x
y
Steady state flow
Transient transport, advection and diffusion
10 years of simulation (timestep = 1 month)
3 faults paths or barriers
23 = 8 possibilities
ꟷ path log10K +2
ꟷ barrier log10K -2
∆ injection well

## Slide 14: First arrival travel times
Scenarios {0,…,7}
ꟷ path
ꟷ barrier
Fault 3 most influential, then Fault 2 then Fault 1
Fault 2 path
Fault 2 barrier
Fault 2 & 3 barriers

## Slide 15: Transport results
Scenario 0
Scenario 1
Scenario 2
Scenario 4
Modflow6 concentrations
X
Y
Z
X
Y
Z
X
Y
Z
X
Y
Z
50 best paths outlets
backward path outlet

## Slide 16: Transport results
cumulated mass
from Modflow6
50 best paths outlets
+
backward path outlet
x

## Slide 17: Flow results
Modflow6 log Darcy velocities (m/d)
Scenario 0
Scenario 1
Scenario 2
Scenario 4
X
Y
Z
X
Y
Z
X
Y
Z
X
Y
Z
50 best paths outlets
backward path outlet

## Slide 18: Computing requirements
From an existing voxet model (140k cells)
  Using Python libraries networkx and flopy
Graph generation: ~30 seconds per graph
Backward or forward distances from graphs: ~ 3 seconds per computation
Modflow6 simulation (1 steady state + 120 timesteps for a total of 10 years): ~ 5 minutes per simulation

## Slide 19: Groundwater application summary
Graph approximations are blind to upstream flow conditions
Backward path approximation seems more accurate
Cumulative mass outlet locations are relatively coherent
Least resistant paths are consistent with the field of Darcy velocity magnitudes

## Slide 20: Future work
Graph weight tuning
First arrival time calibration
Find alternative paths to see if we can approximate the plume shape
What if we used the velocity field rather than the K field to build a graph
Comparison with particle tracking simulations
Unstructured mesh to better explore fault effects
Ideas for other applications and collaboration?

## Slide 21
guillaume.pirot@uwa.edu.au
THANK YOU

## Slide 22: Detailed parameters
Upper hydro stratigraphic unit log10K
    µ = -4.45 m/s
    σ = 0.4 m/s
Middle hydro stratigraphic unit log10K
    µ = -3.10 m/s
    σ = 0.5 m/s
Lower hydro stratigraphic unit log10K
    µ = -4.69 m/s
    σ = 0.6 m/s
Kxx=Kyy=10Kzz
Porosity: 25%
Qwell = 50∙103 m3/d
αL = 1 m (longitudinal dispersivity)
αT = 0.1 m (transvers dispersivity)

## Slide 23: Estimation of first arrival travel time from breakthrough curves
t1 scenario 5